## Slide 1
Introduction to Statics
© 2012 Project Lead The Way, Inc.
Principles of Engineering

## Slide 2: Statics
The study of forces and their effects on a system in a state of rest or uniform motion
©iStockphoto.com
©iStockphoto.com
©iStockphoto.com
Notes: Uniform motion means constant velocity. State of rest is constant velocity also, specifically v=0.

## Slide 3: Statics Principles
  Newton’s First Law of Motion (law of inertia):
  An object in a state of rest or uniform motion will continue to be so unless acted upon by a net force
©iStockphoto.com
Notes: Describes the relationship between velocity and forces.

## Slide 4: Statics Principles
Newton’s Second Law of Motion:
The acceleration of an object is proportional to the net force acting on the object and inversely proportional to the object’s mass
Force = Mass x Acceleration
Notes: Describes the acceleration of an object in the direction of the net force applied to it.

## Slide 5: Statics Principles
Newton’s Third Law of Motion:
For every action force, there is an equal and opposite reaction force
©iStockphoto.com
Notes: Describes action-reaction pairs.

## Slide 6: Equilibrium
Static Equilibrium:
A condition where there is not a net external force acting upon a particle or rigid body and the body remains at rest or continues at a constant velocity
©iStockphoto.com

## Slide 7: Equilibrium
Translational Equilibrium:
The state in which there are no unbalanced forces acting on a body
©iStockphoto.com
©iStockphoto.com
Balanced
Unbalanced

## Slide 8: Equilibrium
Rotational Equilibrium:
The state in which the sum of all the clockwise moments equals the sum of all the counterclockwise moments about a pivot point
©iStockphoto.com
Remember
M = d x F

## Slide 9: Statics Principles
Scalar Quantities: A physical quantity that has magnitude only
Examples: Mass, length, time, volume, temperature, pressure, and speed
©iStockphoto.com
©iStockphoto.com

## Slide 10: Statics Principles
Vector Quantities: A physical quantity that has both a magnitude and direction
Examples: Position, velocity, force, and moment
©iStockphoto.com
©iStockphoto.com

## Slide 11: What Is a Force?
A vector quantity defined by its known magnitude, direction
In addition, the point of application of a vector is important.
A
45 lbf
21.8°NE
The pushing or pulling interaction of objects

## Slide 12: Force Units
British System of Units
pound-force (lbf)
International System of Units
newton (N)
Conversions between Unit Systems
1lbf = 4.448 N
1N = 0.2248 lbf

## Slide 13: Static Equilibrium Force Principles
  Forces always occur in pairs acting on two different objects.
  Force pairs act in opposite directions and have the same magnitude.

## Slide 14: Force Components
A single force can be replaced by component forces if their combination produces the same effect as the original force.
a
Fa
Fay
Fax
a

## Slide 15: Resultant Force
A single force that has the same effect as two or more concurrent forces
2lbf
5lbf
5lbf
2lbf
7lbf
Resultant
3lbf
Resultant
=
=